## Slide 1: IETF DetNet and IEEE 802.1 Time-Sensitive Networking
Status update
IEEE / IETF Coordination Committee, Prague, July, 2017
Norman Finn

## Slide 2: Outline
The common vision
TSN description and status
DetNet description and status
Cooperation status

## Slide 3: TSN and DetNet: a common vision
A DetNet/TSN data stream:
  May be unicast or multicast.
  Has an absolute maximum bandwidth, and uses most of it.
  Requires an absolute upper bound on end-to-end latency.
  Requires 0 congestion loss in the network.
  May require extraordinary protection against random or equipment failures.
  Can afford to make and wait for a resource reservation to obtain these goals.
A small to enterprise-sized network can carry any mix of TSN and non-TSN traffic.
DetNet/TSN applications typically require time synch to < 1 µS.

## Slide 4: Time-Sensitive Networking Task Group
TSN is one of 5 Task Groups of the IEEE 802.1 Higher-layer LAN Protocols Working Group of the IEEE 802 LAN/MAN Standards Committee.
IEEE 802.1 chair: Glenn Parsons. TSN chair: János Farkas.
TSN TG (née AVB TG) has been active since 2005.
Typically, 2/3 of the 50-60 voting members of 802.1 participate in TSN.
Six face-to-face meetings / year, approx. 24-32 hours / meeting
2 hours/week teleconferences.

## Slide 5: TSN completed standards
Amendments to IEEE Std 802.1Q Bridges and Bridged Networks:
  802.1Qat Stream advertisements and resource reservation
  802.1Qav Credit-based shaper
  802.1Qbu Transmission preemption (along with IEEE Std 802.3br)
  802.1Qbv Time scheduled output queues
  802.1Qca Extensions to ISIS for multi-pathing and reservations
  802.1Qch Cyclic Queuing and Forwarding
  802.1Qci Per-Stream Filtering and Policing
Stand-alone IEEE standards:
  802.1AS Timing and Synchronization
  802.1BA Profile for plug-and play AVB networks
  802.1CB Frame Replication and Elimination for Reliability

## Slide 6: TSN standards in progress
Amendments to IEEE Std 802.1Q Bridges and Bridged Networks:
  802.1Qcc Enhancements for stream reservation protocol
  802.1Qcp YANG models for bridges
  802.1Qcr Asynchronous Traffic Shaping
  802.1Qcw YANG models for all TSN queuing and filtering techniques
Stand-alone IEEE standards:
  802.1AS Timing and Synchronization revision and enhancements
  802.1CM Profile for CPRI front-haul networks over bridges
  802.1CS Link-local Registration Protocol

## Slide 7: TSN Acceptance
Increasing interest, actual deployments.
Many vendors, including major bridge/switch vendors, claim compliance with AVB standards.
Multiple vendors are claiming compliance with just-completed TSN standards, including credit-based shapers and cyclic queuing and forwarding.
Active participation in TSN and in industry fora (ODVA, Avnu) by industrial, automotive, infotainment, and audio-video studio users.
IEEE 802.3 has several TSN-specific MAC/PHYs started or starting.
AVB deployment is growing. TSN deployments have commenced.

## Slide 8: TSN issues
Vendors and customers have both been waiting for each other.
Many relatively small vendors of end stations must make a big leap from dedicated digital busses to a protocol stack.
Standards are often ahead of products.
No support for routers.

## Slide 9: TSN summary
A vendor can build a network claiming compliance to TSN standards that meet all of the goals in the “common vision”, above.
There are gaps in management capabilities that hinder interoperability among different vendors, for which projects are now in place to close.
Additional capabilities, as requested by certain verticals, are now in progress.

## Slide 10: IETF Deterministic Networking WG
DetNet is in the Routing Area, AD Deborah Brungard
Charter approved October 5, 2015
Chairs: Pat Thaler, Lou Berger
3 face-to-face meetings / year, 2-3 hours/meeting,
2 hours/week teleconferences
Appreciable, but not heavy, activity on 3 mailing lists

## Slide 11: DetNet status
Two drafts adopted by WG:
  Deterministic Networking Architecture
  Deterministic Networking Use Cases
  One or both may progress from this meeting
Other DetNet drafts:
  4 Additional use cases
  1 Security
  1 Data plane
  2 Information model
  1 Architecture
  1 Control plane
  A few are likely to be adopted from this meeting, especially the data plane draft.

## Slide 12: DetNet issues
Approximately one year behind original milestones.
Standards are often ahead of products.
The target users are still awakening to the value of networking, and to the differences between bridging and routing.

## Slide 13: Cooperation status
Significant common membership
  More than half of active DetNet participants are also active in TSN.
  Official liaisons have not been necessary.
Apparent agreement on L2 vs. L3 data plane issues.
Work on information models (YANG) is just blossoming in both TSN and DetNet.
  There is a potential for conflict; perhaps a mailing list and teleconference series for information modeling is in order.
Potential participants must ask in order to get access to TSN resources.
All in all, cooperation has been very successful.